## Slide 1: Why should your next secure design be PUF based
IPs securing ICs
Vincent TELANDRO, Sales Manager
Christophe TREMLET, Marketing & Sales Director

## Slide 2: Hierarchy in Security Measures
HW
Software cryptography
Human

## Slide 3: Cryptography
Authenticity
The recipient can verify that the sender is who he/she claims to be
Integrity
The recipient can verify that the message has not been altered
Confidentiality
Only the intended recipient of a message can decrypt its contents
Cryptography

## Slide 4: Modern Cryptography
Secret algorithm
1919
Enigma
Public algorithm / Secret key
1971
Lucifer
1975
DES
2000
AES
1999
TDES
1977
RSA
1991
DSA
1992
ECDSA
plaintext
ShiftRows
AES
roundkey(i)
roundkey(N)
roundkey(1)
SubBytes
ShiftRows
MixColumns
SubBytes
ciphertext
for i=1 to N

## Slide 5: Symmetric Cryptography
secret key
secret key
ciphertext
plaintext
plaintext
Encryption
Decryption
Enc ( secret key ; plaintext )
Dec ( secret key ; ciphertext )

## Slide 6: Symmetric Mutual Authentication
Smartcard
Terminal
RNG
“ = “ ?
ID?
K
Yes
Terminal
authenticated
No
Terminal not
authenticated
“ = “ ?
Yes
No
Smartcard
authenticated
Smartcard not
authenticated
Random number?
I
ID
K
RNS
RNS
Enc( K ; RNT|| RNS )
RNT
RNG
ID2K
Enc( K ; RNS|| RNT )
II

## Slide 7: Secret Key – Attacks
PCB
SoC
K
3V
Non-invasive attacks
Invasive attacks
  Chemical & laser etching
  On-chip microprobing
  Layout reconstruction
  Memory content recovery
  Electron Beam Tester (EBT)
  FIB-SEM nanofabrication
  Passive (observation)
  On-board probing
  Side-channel attacks
  Active (perturbation)
  Over/under V, T° or clock
  Voltage, laser, clock or EM glitchs

## Slide 8: Secret Key – Countermeasures
Obfuscation
Bus scrambling
Random P&R
Shield: metal mesh
Power randomisation
Cryptography
Key diversification
Memory encryption
Protect keys
Sensors
Voltage
Temperature
Clock
Laser & EM pulses

## Slide 9: Physical Unclonable Function (PUF)
Principle
Acts as a device fingerprint
Generates a per-chip unique identifier
Exploits the random variations of the devices’ parameters
Challenges
Unclonable: robust against counterfeiting
Uncontrollable: robust against invasive attacks
Unpredictable: robust against reverse engineering
Invariant: stable across voltage, temperature and aging

## Slide 10: PUF – Examples
Memory based
SRAM
Latch
Delay
based
Arbiter
Ring oscillator
Glitch
Process based
VGS or VDS
Via
Arbiter
0
0
1
1
0
1
0/1
I1 < I2
0
t
0
VA
I1 > I2
A=0
I1
VDD
I2
VDD
A
B
VDD
A=1
0
1
0
1

## Slide 11: Invia’s PUF – Principle (patented)
Biasing
Vbias
IA[0:127]
8,16
1,1
1,2
1,16
2,1
8,1
2,2
Digital controller
out
sel
7
Comparator
IB[0:127]
IA
IB
Selector
128-bit register
PUF core
Vbias
VDD
IA
IB
IA[0]
IB[0]
out
IA[127]
IB[127]
sel[0]
sel[127]
1 1 1 0 1 0 0 1
Ibias
…
IB > IA → out = 1
IB ≤ IA → out = 0
Comparator
128-bit register
Biasing
PUF cell 1,1
PUF cell 8,16
Selector

## Slide 12: Invia’s PUF – Characteristics
ΔI = IB – IA
IA
IB
PUF cell - Schematic
MNA
MNB
SA
SB
DB
DA
out = ‘1’
0
out = ‘0’
PUF cell - Layout
MNA
MNA
MNB
MNB
IA
IB
128-bit PUF core
UMC 55 nm
Sigma = 4.5 (1.35 ppm)
Silicon area < 0.01 mm²
Operating cons. < 10 µA
Standby cons. < 10 nA

## Slide 13: Invia’s PUF – Benefits
Benefits
Compact: relatively small silicon footprint
Low-power: consumption significantly smaller than most aternatives
Robust: can be fully simulated at transistor level using a standard flow
Stable: sigma optimized by design; embedded margin check
Secure: active monitoring of the sub-blocks’ integrity (pending patent)
Scalable: the smaller the node, the better the gaussian distribution
Certifiable: can be mathematically modeled

## Slide 14: Takeaways
INVIA, a Thales company
  Conducts exhaustive security audits
  Assists companies in securing their systems
  Delivers silicon-proven IPs part of EAL5+ ASICs
  Protects more than 2.0 billion deployed devices
Thank you for your attention