## Slide 1
RISC-V Helps Getting Your Chip Popular
Frankwell Lin
President
Andes Technology
2019/09/12
IP SoC 2019 Shanghai

## Slide 2
Latest AndeStar™ V5 Lineup
New: Ultra-Compact Low-Power Processors
New: Processors with DSP/P-extension (draft)
New: Processors with Multicore Cache-Coherence
DSA Architecture vs ACE and Examples
Concluding Remarks
Contents

## Slide 3: Andes RISC-V Roadmap
Linux
with FPU/DSP
Fast/Compact
with FPU/DSP
Cache-Coherent
Multicores
A25
N25F, MMU, DSP
Slim and
Efficient
A25MP
1/2/4 A25, L2$,
L1/IO coherence
N25F
V5/32b, FPU, PMP
N22
V5[e], 32/16 GPR
AX25
NX25F, MMU, DSP
AX25MP
1/2/4 AX25, L2$,
L1/IO coherence
NX25F
V5/64b, FPU, PMP
5-stage >1.2GHz
3.58 CoreMark
2.09 DMIPS
2-stage 700MHz
3.95 CoreMark
1.80 DMIPS
D25F
N25F, DSP
Cores with higher total performance and RISC-V ISA extensions
Next
32bit
64bit
Higher performance
Notes: Last but not least I want to give a short overview about our roadmap and our Cores lined up right now, which starts with our N22, a 2 stage pipeline core configurable as Embedded Version with 16 General Purpose Registers or 32 GPRs and capable of 700MHz in a TMSC 28nm process over our medium level N25F core which can include a Floating Point Unit or be configured without as well as options for our previous introduced DSP extension and this is the first core in our roadmap available as 32bit or 64bit core which is also a 5 stage pipeline core over our A-Series, where A stands for application ready and in this case come with an MMU so it can run linux and of course we also offer this as a platform with multiple cores including Level 2 Cache as well as 1st Level Cache coherency and IO coherency. Then we also offer our Cores for 64bit in similar configuration as just discussed.
What we are working on right now is the next stage with bigger pipeline and the Vector Extension, this will be ready soon and announced shortly.
Alright that is our RISC-V roadmap.

## Slide 4
Baseline ISA extensions:
  Faster memory accesses
  Faster branches
  More compact code on top of RV-C
Andes Custom Extension™ (ACE) frameworks for DSA
  Powerful tools
  No CPU design experience needed
PLIC extension:
  Vectored dispatch
  Priority-based preemption
  Save >50% of instructions
  Cache Support:
  Management operations (flush, invalidate, etc.) at the line level
  Uncached accesses
  Write-back and write-through
AndeStar V5: RISC-V + Andes Extensions
  StackSafe™: Stack protection mechanism
  QuickNap™: Fast power-down/wake-up support for caches
  PowerBrake: Digital power throttling
V5: Best Extensions to RISC-V
Notes: Exception redirection to debugger
    Address the limitation of PLIC/CLIC

## Slide 5
AndesCore 22-Series
N22 uCore, PMP
WFI / WFE
HW Bkpt
Interrupt
Intf.
Br. Pred
DSP
FPU
AHBL/APB/FIO
ICache
ACE
PLIC
Debug
PMU
BIU
ILM
DLM
SRAM/AHBL
SRAM/AHBL
Mul/Div
AndeStar V5 or V5e ISA
  Based on RV32-IMC or RV32-EMC
2-stage pipeline, single-issue
AHB-lite system bus
WFI/WFE
Rich baseline options:
  PMP: up to 16 entries
  M-mode, or M+U-mode
  Multiplier: fast or small (1 or 17 cycles)
  Branch prediction: static or dynamic
  I/D Local Memory: 1KiB to 512MiB
  I Cache: 1KB to 32KB; direct-map or 2-way
  HW-handled misaligned load/store

## Slide 6
AndesCore 22-Series
N22 uCore, PMP
WFI / WFE
HW Bkpt
Interrupt
Intf.
Br. Pred
DSP
FPU
AHBL/APB/FIO
ICache
ACE
PLIC
Debug
PMU
BIU
ILM
DLM
SRAM/AHBL
SRAM/AHBL
Mul/Div
Rich baseline options: (cont.)
  Core-Local Interrupt Controller (CLIC)
    >1000 sources, 255 priority levels
    Selective vectoring with priority preemption
    Efficient SW-based tail chaining
  Platform-Level Interrupt Controller (PLIC)
    For multiple cores
    >1000 sources, 255 priorities levels
  Additional buses:
    Fast IO port with 1-cycle latency
    APB private peripheral port
  JTAG debug module
    up to 8 triggers (breakpoints/watchpoints)
    2-wire or 4-wire support
Notes: Slave port and ECC

## Slide 7
CPU Cores | M3 | N22 (same seg config) | M0+ | N22 (same seg config)
ISA | ARM V7m | Andes V5 | ARM V6m | Andes V5e
CoreMark/MHz | 3.34 | 3.97 (+19%) | 2.46 | 3.11 (26%)
DMIPS/MHz (no-inline) | 1.25 | 1.80 (+44%) | 0.95 | 1.11 (+17%)
CSiBE Code Size (KB) | 1,330 | 1,185(-13%) | 1,315 | 1,305
N22 Performance
At 28nm
  Highest frequency: 800MHz (worst case condition)
  Minimal gate count: <15K gates
  Best scores: 3.97 Coremark/MHz, 1.80 DMIPS/MHz (no-inline)

## Slide 8
RV32-P for DSP libraries (>200 DSP functions, 8 categories) |  |  |  |  |  |  |  |  | 
Speedup | Basic | Complex | Ctlr | Filter | Matrix | Ststcs | Xform | Utils | Overall
AVG | 2.67 | 1.86 | 1.34 | 2.3 | 1.7 | 2.87 | 1.38 | 1.21 | 1.92
MAX | 5.71 | 4.65 | 1.78 | 4.73 | 3.04 | 5.66 | 1.96 | 1.69 | 5.71
RV64-P for DSP libraries (under development) |  |  |  | 
Speedup | Basic | Filter | Matrix | Overall
AVG | 5.22 | 2.52 | 3.24 | 3.66
MAX | 12.27 | 5.61 | 6.6 | 12.27
Speedups for various applications (preliminary) |  |  |  | 
Cores | RV64-P |  | RV32-P | 
APP | CIFAR10 (image classification benchmark) | PNET (90% of MTCNN for face detection) | AMR voice codec | MP3 decode
Speedup | 10.7 | 7.64 | 3.67 | 1.84
Speedup with P-Ext on 25-Series

## Slide 9
Designed >150 DSP ISA in the popular Andes V3 cores D10/D15
Donated them as the basis of the P-extension draft for RISC-V
Details:
  Use RV32 and RV64 XLEN-bit GPRs. (i.e. no additional registers)
  Support saturation and rounding.
  Support fixed-point and integer data types.
  SIMD-instructions with 8b, 16b, 32b element size.
  Complex DSP instructions operating on 16-bit, 32-bit and 64-bit data.
  Min, Max, Shift, Byte swap, Bit reverse, Pack, Unpack… operations.
  64-bit signed/unsigned addition & subtraction
  64-bit signed/unsigned multiplication & addition
    E.g., 64 = 64 + 16x16 + 16x16 or
    E.g., 64 = 64 + 32x32
D25F: 25-Series with DSP

## Slide 10
Features | N*25F | A*25
P-Extension | NA | Yes
32KB I$/D$ + 256 BTB | Yes | Yes
SP/DP FPU | Yes | Yes
MMU and S-Mode | NA | Yes
Worst-Case Max. Freq. (GHz)1 | 1.3 | 1.2
Coremark/MHz2 | 3.58 (rv32), 3.52 (rv64) | 
DMIPS/MHz (ground rule)2 | 1.96 (rv32), 2.09 (rv64) | 
1: TSMC 28HPC+ RVT 9T library and high-speed memory. Frequency condition: 0.81v/-40oc. 2: BSP V5.0.0 toolchain; DMIPS/ground rule uses no-inline option. |  | 
Smallest usable N25F/NX25F1: ILM/DLM, no caches/BTB
  N25F @ 1 GHz: 37K, 0.033 mm2, 4.1 uW/MHz
  NX25F@ 1 GHz: 56K, 0.044 mm2, 6.0 uW/MHz
AX25
A25
NX25F
N25F
NX25
IMACFD
Perf Ext.
CoDense
A
C
E
25-Series Processors: Low Power & High Performance

## Slide 11
1/2/4 CPUs (A25 or AX25):
  RV-IMACFD ISA, supporting SMP Linux
  P-extension (DSP/SIMD ISA) draft
Andes Coherence Unit (ACU)
  MESI cache coherence protocol
  Duplicate L1 dcache tags
  I/O coherence for bus masters with no dcache
Bus Interfaces
  AXI bus master interface
  Local memory slave port, for each A25/AX25 CPU
  I/O coherence slave port
  MP subsystem vs. bus interface synchronous N:1 clock ratio
A(X)25MP: Cache-Coherent Multicore

## Slide 12
Bus Master Interface (AXI-128)
Debug I/F
(E.g. to
Debug Xport)
PLIC
I/F
IO Coherence Slave Port
(AXI-64)
Cache Coherence/L2 Cache Controller
AndesCore™ A25MP/AX25MP Multicore
Core 0
PLIC
Core 1
Core 2
Core 3
Debug Transport + Debug Module
M
S
L1-to-L2 64b
ILM
DLM
ILM
DLM
ILM
DLM
D$
I$
D$
I$
D$
I$
I/D LM
Slave Port x4
(AHB-32/64)
Trace
Port
(x4)
ILM
DLM
D$
I$
A(X)25MP: Cache-Coherent Multicore

## Slide 13
L2 Cache Controller (optional)
  0/128/256K…2MB, 32-byte line, 16-way, pseudo random replacement and write-back mode
  ECC error protection, same SECDED capability for L1 caches and I/D local memories
  Tag and data RAMs
    2 tag banks, 8 data banks with bank interleaving
    2-cycle accesses to relieve SRAM timing
  Prefetching
    Load/store: prefetch up to 2/4/8 lines after detecting consecutive linear L2 misses (tracking 8 different address sequences)
    Instruction: prefetch up to 1/2/3 lines after a L2 miss
  Platform Level Interrupt, Debug and Trace Support
  Some key latencies
  L1 read miss/L2 hit: 14 cycles
  2nd of simultaneous transactions of the above: 15 cycles if hitting different banks
  L1 and L2 both read miss: 14 + system memory latency
A(X)25MP: Cache-Coherent Multicore

## Slide 14
AE350_CPU_subsys
AX25MP
AXI bus decoder
System Bus
PLIC
AX25
(Little: +DSP)
vPLIC
IRQ
IRQ
Debug Transport Module
JTAG
Debug Module
AXI
AXI
AXI (IO
Coherent Port)
Debug
Control
AX25MP (B): multicore + L2$, Linux SMP, applications
AX25 (L): unicore+DSP, acceleration control, fast interrupt
CSR
slave port
Normal
path
Power-down
(big) path
LM slave
port (DMA)
LM slave
ports (DMA)
L2 Cache + Mem.
DMA
A(X)25MP: An SoC Example

## Slide 15
Extensibility in RISC-V enables DSA
Acceleration is the key, but 80-20 still applies
  80% of the time spent on 20% of the code/logic
  For rest of the logic, its power & area matter
  For rest of the code, its size matters. So is performance
Baseline processors are important too
An ideal DSA architecture proposed:
  RISC-V standard+ Andes baseline extensions
  + Andes Custom Extension™ (ACE) for your custom instructions
Specific Processors For DSA

## Slide 16
ACE Framework
Automated Env. For
Cross Checking
CPU ISS
(near-cycle accurate)
CPU RTL
Extensible Baseline Components
Compiler
Asm/Disasm
Debugger
IDE
Extended
Tools
- C code
- Verilog
- Attributes
Extended
ISS
Extended
RTL
Test Case Generator
Extended
RTL
Extended
ISS
C O P I L O T
Custom-OPtimized Instruction deveLOpment Tools
- scalar/vector
- background
- wide operands

## Slide 17
ACE 应用

## Slide 18
应用基础: 建立基本核心
Andes RISC-V Core
ISA added by ACE
Andes RISC-V Core
ISA added by ACE
Andes RISC-V Core
ISA added by ACE
Scalar 1
Scalar 3
Scalar 3

## Slide 19
Convolutional logic
Andes RISC-V Core + ACE 应用范例
Scalar1
PE1
PE1
PE1
PE1
PE1
PE1
PE1
PE1
PE1
PE1
PE1
PE1
PE1
Row1 o/p
Row2 o/p
Row n-1 o/p
Row n o/p

## Slide 20
应用范例集
PE1
PE2
PE2
PE2
PE2
PE2
PE2
PE2
128
PE3
PE3
PE3
PE3
PE3
PE3
PE3
PE3
PE3
PE3
PE3
PE3
1024
Deep Learning & Inference
AI Data Center Server
Audio recognition

## Slide 21
Cores | AndeStar™ ISA | GPR bits | Priv. levels | Intr. Ctlr | MMU | I/D$ | ECC | FPU | ACE | DSP (P) | MP
N22 | V5/V5e | 32 | M+U | CLIC |  | I |  |  |  |  | 
N25F | V5 (+RV-FD) | 32 | M+U | PLIC |  | I/D | ü | ü | # |  | 
D25F | V5 (+RV-FD) | 32 | M+U | PLIC |  | I/D | ü | # | # | ü | 
A25 | V5 +RV-FD | 32 | M+U+S | PLIC | ü | I/D | ü | ü | # | ü | 
A25MP | V5 +RV-FD | 32 | M+U+S | PLIC | ü | I/D | ü | ü | # | ü | ü
NX25(F) | V5 (+RV-FD) | 64 | M+U | PLIC |  | I/D | ü | # | # |  | 
AX25 | V5 +RV-FD | 64 | M+U+S | PLIC | ü | I/D | ü | ü | # | ü | 
AX25MP | V5 +RV-FD | 64 | M+U+S | PLIC | ü | I/D | ü | ü | # | ü | ü
V5: RV*IMAC + Andes Extensions, V5e: RV*EMAC + Andes Extensions Common features: PMP, branch prediction, CoDense™, PowerBrake, StackSafe™ 3. ü: included; #: separately licensable |  |  |  |  |  |  |  |  |  |  | 
AndeStar™ V5 Processors

## Slide 22
RISC-V Eco-system is in fast expansion
Andes
  A pure-play processor IP vendor for RISC-V
  Trusted Computing Expert to help shipping billions of SoC
Committed to be your reliable RISC-V CPU IP provider
RISC-V may help getting your chip popular
Concluding Remarks

## Slide 23
Thank you !!