## Slide 1
OTP IP
rorlando@chuangfeixin.com
wangzhigang@chuangfeixin.com
WWW.CFX-Tech.COM
Zhuhai, China
中国智造，创芯中国

## Slide 2: CFX OTP Advantages
Gate Dielectric Anti-Fuse OTP
CMOS Process Compatible – No Additional Masks/Costs
Most Reliable NVM Data Retention – Harsh Environments
Small Die Area
One Time Programmable – Cannot Be Changed
  Closes the “Backdoor” of OTP in other NVM
Ease of Integration

## Slide 3: Gate Dielectric Anti-Fuse
Capacitor Structure using Gate Oxide Dielectric
Applying High Voltage across cap creates oxide breakdown
Oxide Breakdown creates Conductive Path though Oxide
Unprogrammed
Programmed
R > 1G Ohm
R ~ 100K Ohm

## Slide 4: OTP Anti-Fuse
Select transistor
Antifuse
Protected by Patents
CN104681558A 12/3/2013
CN103745977B 4/23/2014

## Slide 5: Gate Oxide Anti-fuse in CMOS
Breakdown voltage is based on Gate Oxide thickness
Standard CMOS process does not have HV transistors
Gate Oxides < 40 Angstroms require Vprog ~ 8 volts
Source “Closing the design gap between system-level and component-level Electro Static Discharge (ESD)”, Scholz, Mirko, 2013/05/29

## Slide 6: Gate Oxide Anti-fuse in CMOS
Device Scaling below 130 nm has reduced programming voltages to < 10 volts
Further Scaling/Vprog reduction makes Dielectric Anti-fuse the OTP of choice
  Standard CMOS Floating Gate becomes impractical
    Gate Oxides are too thin
Standard CMOS process and devices
Ultra Low Power
1T 1C Cell Scales with Process
  Mbit Densities are Practical
High Temperature Operation
  Up to 175 Deg C
Secure
  Non-Alterable
  No Reverse Engineering Contents

## Slide 7: Data Retention- 250 deg C 48h
4Kbits without Deep MPwell

## Slide 8: Data Retention – iRead 24h 250 deg
Before Bake
After Bake

## Slide 9: The Award Nominee
4KB MTP - DB HiTek 110nm 1.5V/3.3V Logic Process
◆ Power Supply
2.8V VDD (±10%)
With internal high voltage charge pump
◆ Memory size 4K-byte
◆ Program Times: 3
◆ Bit Program Operation
◆ Byte Read Operation
◆ Junction Temperature TJ : -40°C ~ 125°C
◆ Data Retention: >10 Years @ 85°C

## Slide 10: 4KB MTP Specifications
◆ MTP Cell :1.5V device
◆ IP Size : 0.283mm^2
◆ Byte Access Time :0.1μs (typ)
◆ Bit Program Time : 0.1ms (typ)
◆ Operating Current :
IVDD_R: 520 μA (typ)
IVDD_P: 920 μA(typ)
◆ Standby Current :
IVDD_SB : 0.1μA(max)

## Slide 11: 512Kb OTP Specifications
Process: Silterra110nm 1.5V/3.3V Ultra Low Leakage Logic Process
Density: 16Kx32bits
Bit Program Operation
32bits Read Operation
Operation Temperature: -40°C ~ 125°C
IP Size: 1340um * 670um
OTP Array
WL Decoder
BL Decoder
Analog Modules
Redundant
Block

## Slide 12: 64Kb OTP Specifications
BL_level_shift
decoder_8to255
decoder_8to255
ARRAY
WL_level_shift
PL_level_shift
TOP_CAP
STM/SA/VB/LS
Decoder 8-255
Process:UMC28nm Logic and Mixed-Mode High Performance Compact Plus Process
Density:64Kbits
Operation Temperature:-40 ℃ ~125℃
Bit Program Operation
IP Size：400um*270um
Bit Read Operation

## Slide 13: Competitive Comparison

## Slide 14: OTP Foundry Status
 | SMIC | Silterra | Dongbu | HLMC | GF | CanSemi | SiEN | UMC | Huahong | GTA | Powerchip | CSMC | Samsung
180nm Logic |  | LV |  |  |  |  | ED |  |  | ED |  | LV | 
180nm BCD |  |  |  |  |  | D |  |  |  |  |  |  | 
160nm HV | P | P |  |  |  |  |  |  |  |  | P |  | 
160nm HV 5V |  | D |  |  |  |  |  |  |  |  |  |  | 
130nm logic | P | LV |  |  |  |  |  |  |  |  |  |  | 
130nm HV |  | P |  |  |  |  |  |  |  |  |  |  | 
110nm Logic |  | SP | D |  |  |  |  |  |  |  |  |  | 
110nm HV |  | P |  |  |  |  |  |  |  |  | P |  | 
90nm BCD |  |  |  |  |  |  |  |  | ED |  |  |  | 
90nm Logic |  |  |  |  |  |  |  |  |  |  |  |  | P
55nm HV | SP |  |  | ED |  |  |  |  |  |  |  |  | 
40nm EHV | ED |  |  |  |  |  |  |  |  |  |  |  | 
40nm Logic | ED |  |  |  |  |  | ED |  |  |  |  |  | 
28nm HKMG |  |  |  | ED |  |  |  | ED |  |  |  |  | 
22nm FDSOI |  |  |  |  | SP |  |  |  |  |  |  |  | 
14nm Logic | ED |  |  |  |  |  |  |  |  |  |  |  | 
Note: |  |  |  |  |  |  |  |  |  |  |  |  | 
ED | Early Development |  |  |  |  |  |  |  |  |  |  |  | 
D | Development |  |  |  |  |  |  |  |  |  |  |  | 
SP | Silicon Proven |  |  |  |  |  |  |  |  |  |  |  | 
RP | Risk production |  |  |  |  |  |  |  |  |  |  |  | 
LV | Low volumn production |  |  |  |  |  |  |  |  |  |  |  | 
P | Production |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 15: CFX OTP Design Flow
We do all the work
You specify the details
  Organization, interface, supply voltages
We provide you with an embeddable block
  IP Merge at Foundry
  Data Sheet
  Interface
  Verilog Model
Complete Solution
  Programming Circuits
  Charge Pumps

## Slide 16: OTP Applications
Logic Output
  Cells are always in Read Mode – Instant On
  Cell Outputs are used as logic signals
  Architecture is n wide x 1 deep
OTP Block
N Outputs
Programming Interface

## Slide 17: OTP Applications
Memory Array
  OTP has Memory Interface
    Read and Program
  Address and Data Bus
  Organized as n x m
OTP Block
Address Bus
Data Bus
Control

## Slide 18: Modern OTP
Traditionally, OTP is programmed in external programmer
Modern Programming Voltages and Currents are Low
Charge Pumps and Programming Circuitry “Built In”
OTP Can be used for On-line, In-Situ Programming
  Opens New Class of Applications

## Slide 19: OTP Applications
OTP is a complimentary technology to other NVM
Traditional Applications
  Serialization
  Product Configuration
  Yield Improvement
  Trimming
  Timing
  Security
Emergence of IoT has creates new OTP Opportunities
  Control of OTA updates
Programmable Analog creates new OTP Opportunities

## Slide 20: OTP is Everywhere
Consumer | Code Storage, ECC and redundancy, Security keys, Configuration | Set top boxes, multimedia SoCs, application processor, gaming, GPS and storage
Mobile | Code Storage, ECC and redundancy, Security keys, Configuration | CMOS image sensor, baseband processor, RF transceiver, power amplifier, display, mobile DRAM, mobile SRAM, power management chipsets
Analog/Mixed Signal | Configuration, Calibration/Trimming | Amplifiers, ADCs/DACs, PLLs, audio/Display drivers, PMUS and telecommunications
Industrial | Code Storage, ECC and redundancy, Security keys, Configuration | Sensors, motor control, MCU, RFID, power control and video surveillance
Automotive | Code Storage, ECC and redundancy, Security keys, Configuration, Calibration/Trimming | Control systems, DSPs, in-car communication and in-car entertainment system
Mission-critical | Code Storage, ECC and redundancy, Security keys, Configuration, Calibration/Trimming | High-speed Rail/Aircraft/Satellite/Cruise missile/Space shuttle control

## Slide 21: Product Configuration
SOC Tooling is Becoming Expensive
Different Applications or Usage Cases Create Proliferation
OTP Allows Configuration Selection
  Single Mask Set
  Single Test Platform
  Higher Volumes, Lower Costs

## Slide 22: Yield Improvement
Single Processing Defects can affect large blocks(Array Based)
  Memory(DRAM/SRAM)
  Image Sensors
  Logic(Gate Arrays)
  Column Drivers
OTP is used at Test to map in redundant rows/columns
Increase Yields

## Slide 23: Timing
Oscillator Trimming
  Eliminates process variation
Frequency Selection
  Clock Divider Selection

## Slide 24: Security
Unique Product Identifier
Encryption Passwords
Standardized Security Schemes
  HDMI
  WiMax
  BlueRay

## Slide 25: RF Tags
High Security
Read on Power Up
Low Power During Read is Critical
  Ultra Low Sleep Power
Low Power During Program
Program All Locations to Disable

## Slide 26: Analog IC Design Challenges
CMOS Process Variation
  Inductor +/-1%
  Gate Capacitance +/-5%
  MIM Capacitance +/-15%
  Parasitic Capacitance +/-15%
Next to Impossible To Design Analog in CMOS without Trim

## Slide 27: Analog IC design
More and More Analog is Implemented in Standard CMOS
  SOC including Analog Block
  Interface is often Analog Intensive
  High Speed Digital is Analog
Advanced CMOS Process Manufacturing Variations
  Difficult to Meet Desired Analog Specifications
Trimming is Required to Meet IC specifications
Calibration is Required to Meet System Specification
OTP is ideal for both

## Slide 28: Programmable Analog
One Chip can be used for multiple designs
Compensates for variation in system requirements
Examples
  Voltage Levels
  Timers
  Sensing Inputs

## Slide 29: Prog. Analog - Battery Management
Compensate for Variation in Battery Architecture and Chemistry
  Charging Current
  Charging Voltage
  Charging Profile
  Voltage Sensing Levels

## Slide 30: Prog. Analog- Display Driver
Compensate for Panel Model Variation
  Gamma Curve
Compensate for Panel Manufacturing Process Variation
  VCOM Setting
  Gamma Calibration

## Slide 31: Prog. Analog- PMIC
Output Voltage Levels
Sequencing and Timing
Voltage Sensing Levels – Resets
Ramp Rates
Alarms
  Overcurrent Limits
  Temperature Limits

## Slide 32: Prog. Analog- Programmable Vref
Eliminates traditional external voltage Divider
Eliminates Variations
  Resistor Tolerance
  Chip-to-Chip Variations

## Slide 33: OTP in IoT
OTA updates key feature
  Product improvements, bug fixes
Open the door to hacks
OTP is used as Primary Boot
  Cannot Be Changed
  OTP Used as Code Revision Counter
Insures the Integrity of the Code

## Slide 34: CFX OTP IP
Standard Logic CMOS Process ;
Simple Integration Flow ;
Scalable from 350 to <10 nm ;
In-System Programmable ;
High Reliability (> Mil Spec) ;
Secure ;
High Density ;
Low Cost ;
Patent Protected ;
Volume Proven (>1B served, like McDonalds) ;
Local Support Zhuhai, Beijing, Shenzhen) ;
创芯中国 ;

## Slide 35: CFX OTP IP - A Worldwide Sensation
OTP IP Devices
1 Billion